## Slide 1: ArduPilot SITL — Windows Install
WSL2 + Ubuntu method • plus PC bridge to ESP32
(Prepared for your boat control workflow)

## Slide 2: What you’ll set up
ArduPilot SITL (Simulator) running on Windows via WSL2 (Ubuntu)
PC-side ESP32 bridge: Serial ⇄ ESP‑NOW
Python bridge: MAVLink ⇄ Serial (commands + telemetry)
Mission Planner / QGroundControl talking to SITL

## Slide 3: Prerequisites
Windows 10/11 with admin rights
≈ 10 GB free disk space, stable internet
Arduino IDE (for ESP32 bridge firmware)
Python 3 on Windows (for the MAVLink bridge)

## Slide 4: Install WSL + Ubuntu (PowerShell as Administrator)
wsl --install -d Ubuntu # Reboot when prompted and create your Ubuntu username/password
This installs the Linux subsystem and Ubuntu userland once.

## Slide 5: Inside Ubuntu (WSL): install prerequisites & clone ArduPilot
sudo apt update && sudo apt install -y git git clone https://github.com/ArduPilot/ardupilot.git cd ardupilot git submodule update --init --recursive ./Tools/environment_install/install-prereqs-ubuntu.sh -y . ~/.profile
The last line reloads environment variables set by the installer.

## Slide 6: Run SITL (Rover example)
cd ~/ardupilot/ArduRover ../Tools/autotest/sim_vehicle.py -v Rover --map --console --out=udp:127.0.0.1:14550
The --out sets the MAVLink stream to the port your Python bridge uses.

## Slide 7: Windows: Python bridge setup
pip install pymavlink pyserial # Edit ap_bridge.py constants: SERIAL_PORT = "COM12" # set to your ESP32 bridge COM port BAUD = 115200 SITL_ENDPOINT = "udp:127.0.0.1:14550" # Then run: python ap_bridge.py
Make sure Arduino Serial Monitor is closed so Python can open the COM port.

## Slide 8: Flash PC-side ESP32 bridge (PCBridge.ino)
Board: ESP32 Wrover Module (ESP32 core installed)
Upload PCBridge.ino to the ESP32 connected to your PC
Open Serial Monitor @ 115200 and confirm: {"type":"pcbridge","status":"ready"}
Find COM port in Windows Device Manager
  Use that COM in ap_bridge.py (SERIAL_PORT)

## Slide 9: Verify data flow
SITL → Python → ESP32 bridge → ESP‑NOW → Boat
  SITL generates SERVO_OUTPUT_RAW / RC overrides
  Python prints logs & forwards commands: C <servo_us> <duty>
Boat → ESP‑NOW → ESP32 bridge → Python → SITL
  Boat sends telemetry as NDJSON
  Python converts to MAVLink GPS_INPUT + BATTERY_STATUS

## Slide 10: Mission Planner / QGC
Connect to SITL (auto-detected on localhost)
Open Radio/Output screens to see channels move
CH1 controls steering (servo_us), CH3 controls throttle (duty 0..1023)

## Slide 11: Troubleshooting
No serial data in Python
  Wrong COM port; close Arduino Serial Monitor; check Device Manager
No SITL heartbeat
  Ensure --out=udp:127.0.0.1:14550; firewall; SITL running in WSL
Boat not reacting
  Both ESP32s powered; MAC/broadcast ok; ESP‑NOW paired; correct GPIO pins
Permissions (WSL)
  Run commands inside Ubuntu; use your normal (non-root) user

## Slide 12: Useful commands (WSL / System)
# WSL wsl -l -v # list distros wsl --shutdown # restart WSL engine # Update ArduPilot sources cd ~/ardupilot && git pull && git submodule update --init --recursive # Different vehicle targets cd ~/ardupilot/ArduPlane # or ArduSub/ArduCopter/etc. ../Tools/autotest/sim_vehicle.py -v ArduPlane --map --console --out=udp:127.0.0.1:14550

## Slide 13: Wrap up / Next steps
Tune channel mapping or add more channels (Python bridge)
Feed additional telemetry (e.g., current sensors, GPS accuracy)
Optionally move to CRSF/MAVLink-over-ESP‑NOW later